FOR IMMEDIATE RELEASE

02 February 2011

Alfa ROMEO introduces new 2.0 JTDM-2 140 bhp diesel engine to Giulietta range

The sporty Alfa Giulietta five-door hatchback range has just been boosted by the addition of another ultra frugal yet high performing second generation MultiJet diesel engine.

The new 2.0 JTDM-2 140 bhp is an ideal engine for both company car drivers and private owners requiring low fuel consumption and low running costs combined with driving comfort for long trips.

The new engine is equipped with the latest generation JTDM-2 MultiJet Common Rail system that is already present on the 1.6 JTDM-2 (105 bhp) and the 2.0 JTDM-2 (170 bhp) power units. The system represents the most technologically advanced solution for controlling high injection pressures (around 1600 bar) independently of engine RPM and quantity of fuel injected.

Advanced engine management guarantees particularly smooth engine operation in all situations.

This technology, combined with an electronically controlled variable geometry turbocharger, guarantees excellent torque delivery: 350 Nm at just 1750 rpm (with the D.N.A. selector in Dynamic position) and 320 Nm at 1500 rpm (in Normal) – giving it the highest torque in its class compared to similarly efficient and powerful engines.

This new Alfa Romeo Giulietta features reduced CO2 emissions and reduced fuel consumption (119 g/km and 62.8 mpg respectively in the combined cycle), a top speed of 127 mph and acceleration from 0 - 62 mph in 9 seconds. The engine is designed for customers who appreciate excellent throttle response but are also concerned with fuel consumption and running costs. In real terms, with a 13% BIK (Benefit in Kind) rate, 40% tax bracket company car drivers will pay as little as £90 a month in company car tax for the Lusso trim version.

On the theme of environmental respect, the engine is Euro 5 compliant and is equipped with DPF (Diesel Particulate Filter) and Start&Stop as standard. Moreover, advanced exhaust gas treatment technologies have been used, namely a close coupled diesel particulate filter and a built-in EGR (Exhaust Gas Recirculation) system that improves control of temperature and gas flow, simultaneously guaranteeing lower emissions and reduced fuel consumption.

Lastly, the 2.0 JTDM-2 140 bhp boasts a particularly long servicing interval, thus minimising work required on the vehicle during its life cycle and cutting its running costs. The fact that the car only needs servicing every 21,000 miles is a testament to the high quality levels achieved and the efforts made to improve durability and efficiency even further, by means of careful work on individual components.

TECH SPEC

|  | 2.0 JTDM-2 140 bhp |
| --- | --- |
| CHARACTERISTICS |
| No. of cylinders, arrangement | 4 in line |
| Bore x stroke (mm) | 83 x 90.4 |
| Displacement (cc) | 1956 |
| Compression ratio | 16.5 :1 |
| Max. power output: bhp (kW-EC) at rpm | 140 (103) 3750 |
| Peak torque: Nm (kgm-EC) at rpm (NORMAL) | 320 (32.5) 1500 |
| Peak torque: Nm (kgm-EC) at rpm (DYNAMIC) | 350 (35.6) 1500 |
| ELECTRICAL SYSTEM (12V) |
| Battery: capacity (Ah) / Generator (A) | 72 / 600 |
| TRANSMISSION |
| Drive | Front |
| Number of gears | 6 + 1R |
| TYRES |
| Standard version | 205/55 R16 |
| STEERING |
| Steering system | Rack and pinion with power steering |
| Turning circle (m) | 10.9 |
| SUSPENSION |
| Front | MacPherson independent with anti-roll bar |
| Rear | Multilink system |
| BRAKES - (DISCS) |
| Front (mm) | 305 |
| Rear (mm) | 264 |
| WEIGHTS - TANK CAPACITY |
| Fuel tank capacity (litres) | 60 |
| Kerb weight DIN (kg) | 1320 |
| Max towable weight (kg) | 1300 |
| PERFORMANCE |
| Top speed mph (km/h) | 127 (205) |
| Acceleration (driver + 30 kg): 0 - 62 mph (s) | 9.0 |
| FUEL CONSUMPTION - EMISSIONS* |
| urban cycle mpg (l/100km) | 50.4 (5.6) |
| extra urban cycle mpg (l/100km) | 72.4 (3.9) |
| combined cycle mpg (l/100km) | 62.8 (4.5) |
| Exhaust emissions - CO2 (g/km) | 119 |
| Emissions Standard | EURO 5 |

PRICE LIST

Alfa Romeo Giulietta – January 2011

|  | Basic Price | VAT | Retail Price | OTR Charges | Total OTR | BIK Rate (Benefit in Kind) |
| --- | --- | --- | --- | --- | --- | --- |
| 2.0 JTDM-2 140 bhp Lusso | £16,787.06 | £3,357.41 | £20,144.47 | £605.53 | £20,750.00 | 13% |
| 2.0 JTDM-2 140 bhp Veloce | £17,870.39 | £3,574.08 | £21,444.47 | £605.53 | £22,050.00 | 13% |

ENDS

Head office contacts:

Ross Milton, Press Officer on 01753 571717 or email ross.milton@alfaromeo.com or Anna Angelini, PR Manager, Alfa Romeo UK on 01753 571717 or email anna.angelini@alfaromeo.com  or Peter Newton, PR Director, Fiat Group Automobiles UK Ltd on 01753 511431 or email peter.newton@fiat.com

62859/020211